Auxiliary Idler Kit

2007 & Newer Shelby GT500

Metco Motorsports PN MSI-90D

Note to Installer:  All work should be performed on a suitable, level surface.  The negative battery cable should be disconnected while this installation is performed.

- Depress the tensioner arm for the supercharger drive and remove the belt from the supercharger pulley.

- Remove the three bolts from locations A, B & C as shown in Picture 1.  Do not remove the two bolts identified as ‘D’ in Picture 1.

- The three stand-offs fit the back side of the idler bracket plate and mount to bolt locations A, B & C.  Apply blue Loctite to the ends of the provided M6 x 90mm socket-head fasteners, and slide each bolt through the bracket and through the provided bracket standoffs.  Tighten these bolts securely using a 5mm allen bit, but use caution not to overtighten.

- Re-install the supercharger belt, and confirm that there is adequate clearance for the belt at location E as shown in Picture 2.

When using this idler kit with our 2.60” supercharger pulley, a belt that is the same length as the original is appropriate.